list of items

| № | Description | Standard | uom | qty |
| --- | --- | --- | --- | --- |
| İlmələr və çaloklar (Polad) |
| 1 | 4-arm sling (strop) - 4SK 10.0/6000 or equivalent Lifting capacity 10 tons, diameter 21mm, length 6 meters Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 6 |
| 2 | 4-arm sling (strop) - 4SK 10.0/8000 or equivalent Lifting capacity 10 tons, diameter 21mm, length 8 meters Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 6 |
| 3 | 4-arm sling - 4SK 16.0/8000 or equivalent Lifting capacity 16 tons, diameter 27mm, length 8 meters Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 2 |
| 4 | 4-arm sling (strop) - 4SK 5.0/4000 or equivalent Lifting capacity 5 tons, diameter 16mm, length 4 meters Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 5 |
| 5 | 4-arm sling (strop) - 4SK 5.0/2000 or equivalent Lifting capacity 5 tons, diameter 16mm, length 2 meters Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 5 |
| 6 | 4-arm sling (strop) - 4SK 5.0/3000 or equivalent Lifting capacity 5 tons, diameter 12mm, length 3 meters Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 5 |
| 7 | Steel Loop - USK1-1.0/1500 or equivalent Lifting capacity 1ton, length 1.5 meters, diameter 10mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 30 |
| 8 | Steel Loop - USK1-1,3/1000 or equivalent Lifting capacity 1.3 tons, length 1.0 meters, diameter 12mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 29 |
| 9 | Steel Loop - USK1-1,3/2000 or equivalent Lifting capacity 1.3 tons, length 2.0 meters, diameter 12 mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 30 |
| 10 | Steel Loop - USK1-1.6/4000 or equivalent Lifting capacity 1.6 tons, length 4.0 meters, diameter 12 mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 2 |
| 11 | Steel Loop - USK1-1,3/6000 or equivalent Lifting capacity 1.3 tons, length 6.0 meters, diameter 12 mm Rope material: Steel-20 or equivalent Safety factor : 6:1 | ГОСТ Р 58753-2019 | PCS | 30 |
| 12 | Steel Loop - USK1-1,3/8000 or equivalent Lifting capacity 1.3 tons, length 8.0 meters, diameter 12 mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 25 |
| 13 | Steel Loop - USK1-1.6/3000 or equivalent Lifting capacity 1.6 tons, length 3.0 meters, diameter 14 mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 30 |
| 14 | Steel Loop - USK1-2.5/4000 or equivalent Lifting capacity 2.5 tons, length 4.0 meters, diameter 14 mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 30 |
| 15 | Steel Loop - USK1-2.5/2000 or equivalent Lifting capacity 2.5 tons, length 2.0 meters, diameter 16mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 25 |
| 16 | Steel Loop - USK1-2.5/4000 or equivalent Lifting capacity 2.5 tons, length 4.0 meters, diameter 16mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 35 |
| 17 | Steel Loop - USK1-2.5/6000 or equivalent Lifting capacity 2.5 tons, length 6.0 meters, diameter 16 mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 7 |
| 18 | Steel Loop - USK1-2,8/6000 or equivalent Lifting capacity 2.8 tons, length 6.0 meters, diameter 18mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 10 |
| 19 | Steel Loop - USK1-2,8/4000 or equivalent Lifting capacity 2.8 tons, length 4.0 meters, diameter 18mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 13 |
| 20 | Steel Loop - USK1-3,2/3000 or equivalent Lifting capacity 3.2 tons, length 3.0 meters, diameter 19mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 12 |
| 21 | Steel Loop - USK1-3,2/4000 or equivalent Lifting capacity 3.2 tons, length 4.0 meters, diameter 19mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 20 |
| 22 | Steel Loop - USK1-4.0/3000 or equivalent Lifting capacity 4 tons, length 3.0 meters, diameter 22mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 20 |
| 23 | Steel Loop - USK1-4.0/4000 or equivalent Lifting capacity 4 tons, length 4.0 meters, diameter 22mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 15 |
| 24 | Steel Loop - USK1-4.0/5000 or equivalent Lifting capacity 4 tons, length 5.0 meters, diameter 22mm Rope material: Steel-20 or equivalent Safety factor : 6.1 | ГОСТ Р 58753-2019 | PCS | 4 |
| 25 | Steel Loop - USK1-4.0/6000 or equivalent Lifting capacity 4 tons, length 6.0 meters, diameter 22 mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 4 |
| 26 | Steel Loop - USK1-4.0/8000 or equivalent Lifting capacity 4 tons, length 8.0 meters, diameter 22mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 12 |
| 27 | Steel Loop - USK1-8.0/10000 or equivalent Lifting capacity 6.3 tons, length 8.0 meters, diameter 27mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 12 |
| 28 | Steel Loop - USK1-6,3/8000 or equivalent Lifting capacity 8 tons, length 10.0 meters, diameter 32 mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 2 |
| 29 | Steel Loop - USK1-2.0/3000 or equivalent Lifting capacity 2 tons, length 3.0 meters, diameter 16.5 mm Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 6 |
| 30 | 4-arm sling (strop) - 4SK 3.2/3000 or equivalent Lifting capacity 3.2 tons, diameter 12mm, length 3 meters Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 2 |
| 31 | 4-arm sling (strop) - 4SK 6,3,0/2000 or equivalent Lifting capacity 6.3 tons, diameter 16mm, length 2 meters Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 2 |
| 32 | 4-arm sling - 4SK 6,3,0/4000 or equivalent Lifting capacity 6.3 tons, diameter 16mm, length 4 meters Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 2 |
| 33 | double loop - 2СК 4/8000 or equivalent Lifting capacity 4 tons, diameter 18mm, length 8 meters Rope material: Steel-20 or equivalent Safety factor: 6:1 | ГОСТ Р 58753-2019 | PCS | 2 |